Angular cuts of 9 deg
- 115_124
- 124_133
- 133_142
- 142_151
- 151_160

---
With Carbon in red (unscaled)

---
Carbon scaled to 3.0

---
If drawn on same y-axis value

---
Fitted all with same landau (5th)

---
Carbon normalization
- Thickness CD2 → 0.5 mg/cm2
- Thickness C → 4 mg/cm2
- Contribution of C in CD2 = 75% (so eff. thickness is now 0.5 * 0.75 = 0.375 mg/cm2) for the Carbon…
- To take care of this in pure C run… scale → 4.0 / 0.375 = 10.67
- So the scaling factor because of thickness is 0.375 / 4.0 =
              - 0.09375

---
Carbon normalization
12 hrs C at 2E5 → 8.64 E9 events	CD2 with multiple runs → 4.3 E10
- Factor = 4.97

---
Carbon normalization
12 hrs C at 2E5 → 8.64 E9 events	CD2 with multiple runs → 4.3 E10
- Factor = 4.97
  Total factor then becomes 4.97 * 0.09375 = 0.466

---
Carbon ex fit with pol3, rebin(8)
Scaled the C-fit by 6.0 with same binning
Scaled the C-fit by 15.0 with same binning
Scaled the C-fit by 11.0 with same binning

---
0.21
0.49
0.17
0.25
0.25
0.29

---
Procedure in mind
1. I take a background by eye for total ex. and individual angular ex (same BG for all angles).
2. Try to fit and constrain peaks by looking all 6 plots (5 angles and 1 full) so that the least chi sq is achieved for all of them.
3. Take these peaks as fixed and then fit with a better background (maybe with good Carbon and simulated phase space).

---
(1) Background selection
total
Cut1
cut2
cut3
cut5
cut4
Up to region 4, the same parameters for the BG seem okay… but for reg5, the stats become less and the same BG can’t be used anymore… Results from this background will be super ugly but still good I think.

---
2.278 looks pretty clear in the (secret) paper… and we also seem to have something at about 2.3…. so adding that in ours

---
It looked like there was something at 1.5 too. Even if not, it helps fitting it better.

---
This region
Needs 4 peaks in my
Opinion… (marked)

---
After the 4 peaks in the end… it still looks like there is need for one more at the marked place… I show the angular ones on the next page with this mark.
The energies I will on the last slide after all are fitted.
Rchi → Reduced chi sq

---
Angular cuts of 9 deg
- 115_124
- 124_133
- 133_142
- 142_151
- 151_160

---
Full ex. spectrum
MeV*, Energy, sigma

---
Initial guess: 915 keV (from Ozge)
Breathing room: 10 keV (915 ± 10)
Ends up at: 905 keV
Restriction on sigma: 150 to 300 keV
Ends up at: 190 keV
Initial guess: 1500 keV (added)
Breathing room: 200 keV (1500 ± 200)
Ends up at: 1465 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 150 keV
Initial guess: 1866 keV (from Ozge)
Breathing room: 10 keV (1866 ± 10)
Ends up at: 1859 keV
Restriction-sigma: 150 to 250 keV
Ends up at: 160 keV
Initial guess: 2280 keV (from the paper)
Breathing room: 10 keV (2280 ± 10)
Ends up at: 2270 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 200 keV
Initial guess: 2550 keV (from Ozge)
Breathing room: 20 keV (2550 ± 20)
Ends up at: 2564 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 200 keV
-10 keV

---
Initial guess: 2875 keV (from Ozge)
Breathing room: 15 keV (2875 ± 15)
Ends up at: 2860 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 150 keV
Initial guess: 3300 keV (added)
Breathing room: 200 keV (3300 ± 200)
Ends up at: 3259 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 150 keV
Initial guess: 3800 keV (from paper)
Breathing room: 20 keV (3800 ± 20)
Ends up at: 3780 keV
Restriction-sigma: 150 to 250 keV
Ends up at: 250 keV
Initial guess: 4057 keV (from Ozge)
Breathing room: 10 keV (4057 ± 10)
Ends up at: 4067 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 150 keV
Initial guess: 4270 keV (added)
Breathing room:300 keV (4270 ± 300)
Ends up at: 4462 keV
Restriction on sigma: 150 to 250 keV
Ends up at: 240 keV
-10 keV

---
Initial guess: 4800 keV (added)
Breathing room: 300 keV (4800 ± 300)
Ends up at: 4934 keV
Restriction-sigma: 150 to 250 keV
Ends up at: 150 keV
-10 keV

---
115_124
MeV*, Energy, sigma

---
124_133
2
MeV*, Energy, sigma

---
133_142
3
MeV*, Energy, sigma

---
142_151
MeV*, Energy, sigma

---
151_160
MeV*, Energy, sigma