Analysis Status Meet
November 20th, 2025

---
(d,p) excitation function
Total E* plot
E* > S(n)
E* < S(n)
Deuteron Breakup component
Exogam
Drift Chamber
Trajectories: CATS
Counts/20keV
G.S.
2.5 MeV
Carbon
S(n)
4.6 MeV
Ex (MeV)

---
The need for CATS
DSSD
Light
Correction for dead layer
Correction for target
θ3
θ4
Heavy
DC X,Y
CATS1, 2
Ozge’s method: Shift the target spot to minimize the resolution in E* plot
BeamImpact = TVector3(-(CATS->PositionOnTargetX)+1.7,-(CATS->PositionOnTargetY)+2.3,0);

---
CATS calibration
cats:# CATS 1 CATSNumber: 1
X01_Y01: 42.9372 -42.6154 -1587.1 mm
X28_Y01: -28.0790 -41.6154 -1587.1 mm
X01_Y28: 42.9372 29.5046 -1587.1 mm
X28_Y28: -28.0790 29.5046 -1587.1 mm
cats: #CATS 2 CATSNumber: 2
X01_Y01: 33.5929 -38.1093 -1090.1 mm
X28_Y01: -37.4981 -38.1093 -1090.1 mm
X01_Y28: 33.5929 33.0107 -1090.1 mm
X28_Y28: -37.4981 33.0107 -1090.1 mm
Known from surveyor:
the pos of central holes only

---
CATS calibration→ mask central holes (x,y)

---
CATS calibration→ target mask holes (x,y)
Acc. To Surveyor
Off by about 3 mm in X and 2 mm in Y
Rotated----------->

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ target mask holes shift (x,y)
New shifts (Δ = surveyor - measured)
Hole 1 (X, Y): (0.18, 0.32)
Hole 2 (X,Y): (-0.15, 0.04)
Hole 3 (X,Y): (-0.14, 0.06)
Hole 4 (X,Y): (-0.04, -0.21)
Acc. To Surveyor
1
2
3
4

---
Drift Chamber : Construction
4 channels in total, 2 horizontal and 2 vertical
anode

---
Drift Chamber: working
Drift time
Most events
Electron drifts
More drift time
Anode wire
More events
And more D.T.

---
Drift Chamber: Channel identification
Conclusion:
DC4 is left
DC_4 Energy
-DC_3 Energy

---
Drift Chamber: Channel identification
Conclusion:
DC3 is right
DC_4 Energy
-DC_3 Energy
Dc4
Dc3
Dc2
Dc1

---
Drift Chamber: Channel identification
More drift time
Counts in log scale

---
Drift Chamber: Drift time spectra

---
Drift Chamber: Drift time spectra

---
Drift Chamber: Trajectory by CATS
-1090.1 mm
-1587.1 mm
1260.9 mm
Drift time combined
Hole 0 mm
Y Position on DC by CATS

---
Drift Chamber: CATS cons. vs Drift time

---
Drift Chamber: Spot on DC1

---
E* < S(n)

---
E* < S(n)
115-124
124-133
133-142
142-151
151-160

---
E* < S(n): Resolution
Gamma rays can help identify and constrain states.
For that, we gate on a definite value of Ex and see the gamma rays.
The resolution of EXOGAM will depend on 3 factors:
The intrinsic resolution.
The angle uncertainty
Beta spread of the beam
Thesis: Stephane Leenhardt (2000)

---
Exogam: Resolution
Beta = 0.18, sigma(beta) = 0.003
Angles = 90, 135 degrees
Sigma (angles): taken 27.5 mm pitch with 140 mm target to crystal distance

---
Exogam: Resolution
For example: @ 2033 keV from 68Ni, FWHMint = 3.44
Total FWHM = 43.8

---
Exogam: Resolution
FWHM = 36 +- 4 keV

---
To-do/Ongoing Work:
Implementing this Drift Chamber with multiplicity > 0 with preference given to events predicted by CATS.
Build the angular correlation of light and heavy.
Building the excitation plot with new positions of CATS.
Then move on to the gamma vs E*.

---
The 594 keV transition: whether to include in the fit
Should have sigma ~ 5.5 keV

---
594: zoomed in

---
CATS calibration→ cats mask holes shift (x,y)
If this is 594, with the sigma value of 5.5keV I count the yeild for 594 +- 16
With gates on slices of E* spectrum.

---
Drift Chamber: Channel identification
Carbon reaction with 68Ni will appear differently in TACs because of heavier residual nucleus.
Theta heavy vs theta light and effect of Carbon.
ϴ

---
Backup

---
Drift Chamber: Channel identification

---
Drift Chamber: Channel identification

---
Drift Chamber: Channel identification

---
Drift Chamber: Channel identification

---
Drift Chamber: Channel identification

---
Drift Chamber: Channel identification

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
CATS calibration→ cats mask holes shift (x,y)

---
Drift Chamber: Channel identification