F135degree-F90degree
clovers
energy
Efficeincy135 - Effciciency90
F12
F4
F3
F5
F13
F6
F7
F8
F11
F10
F2
F9
Efficiency differences in 90 degree detectors and 135 degree detectors which are side by side (same Phi angle).
The efficiency lost is higher in low energy than high energy. That explains the target holder effect.
Theta	Phi	Clover
135.000000 -90.000000 !Flange 2
 135.000000 90.000000 !Flange 3
 135.000000 0.000000 !Flange 4
 135.000000 180.000000 !Flange 5
 90.000003 90.000000 !Flange 6
 90.000003 135.000000 !Flange 7
 90.000003 180.000000 !Flange 8
 90.000003 -135.000000 !Flange 9
 90.000003 -90.000000 !Flange 10
 90.000003 -45.000000 !Flange 11
 90.000003 0.000000 !Flange 12
 90.000003 45.000000 !Flange 13

---
Clover efficiency
1cm Al absorption corrected for 135 degree clovers
Energy
Clover Efficiency %
Energy	Al 1cm	5 cm
121	0.65	0.12
244	0.73	0.21
344	0.76	0.26
778	0.82	0.39
963	0.84	0.42
1408	0.86	0.49

---
dash lines with 1cm Al material absorption
eff c135-c90