TOF calculation
Used runs:
68Ni
Run507 in exp. data = Run432 in Lise data
Lise++ file : e843_extended_Ok_Foc62_Run432.lpp
Information from LISE online notes:
Run 432 (68Ni with wedge @ ~ 40 MeV/A) -> F31 to +3/+13; F43 to +-15; F51 = -17/+25; Brho2_RMN = 2.1687 => Brho2_L++ =2.1671
Used runs:
68Ni beam:
Run503 in exp. data = Run424 in Lise data
Lise++ file : e843_extended_Ok_Foc62_Run425.lpp
Information from LISE online notes:
Run 424 (68Ni without wedge)
-> F31 to +4/+13; F43 to +-15; Brho2_RMN = 2.5126 => Brho2_L++ =2.5107

---
T-CATS1-D4
			Notebook values			calculated				channels
Runexp	RunLISE	isotope	brho	Energy	velocity	distance cm	TOF catsd4	distance cm	TOFDD6-DD4	Cats-D4	DD6-DD4
507	432	68Ni	2.1671	37.7436	8.28462	2639	318.542069521595	2150	259.51703276	17240.0	32035.0
507	432	67Ni	2.1671	37.7436	8.39881	2639	314.211179917155	2150	255.9886460105	17416.0	32035.0
503	425	68Ni	2.5107	50.32794	9.47515	2639	278.518018184409	2150	226.9093365276	18914.8
503	425	67Ni	2.5107	51.80388	9.60235	2639	274.828557592673	2150	223.9035236166	19043.0

---
			Notebook values			calculated				channels
Runexp	RunLISE	isotope	brho	Energy	velocity	distance cm	TOF catsd4	distance cm	TOFDD6-DD4	Cats-D4	DD6-DD4
507	432	68Ni	2.1671	37.7436	8.28462	2639	318.542069521595	2150	259.51703276	17240.0	32035.0
507	432	67Ni	2.1671	37.7436	8.39881	2639	314.211179917155	2150	255.9886460105	17416.0	32035.0
503	425	68Ni	2.5107	50.32794	9.47515	2639	278.518018184409	2150	226.9093365276	18914.8
503	425	67Ni	2.5107	51.80388	9.60235	2639	274.828557592673	2150	223.9035236166	19043.0
2639
2150

---
slope	gain	Channel / Slow down	tof	L	velocity	Beam E	MG_Ex
-0.024050	732.91	12352.1	435.847	2639	6.054877	19.60022	2 MeV
cats-d4-zdd L26
cats-d4-zdd L26

---
slope	gain	channel	tof	L	velocity	Beam E	MG_Ex
-0.019593	597.109	12352.1	355.085	2150	6.054877	19.60022	2 MeV
cats-d4 with L 21 m

---
Second method using only one run and tac calibrator slope,
finding Time refarance 0

---
T-CATS1-D4
TOF = (Time_0_ref - TAC_CATS1_D4)*slope
			calculated				channels		Time 0 ref
Runexp	RunLISE	isotope	distance cm	TOF catsd4	distance cm	TOF L21	Cats-D4	Slope	L26	L 21
507	432	68Ni	2639	318.542069521595	2150	259.51703276	17240.0	0.02554	29712.2	27394.2
503	425	68Ni	2639	278.518018184409	2150	226.9093365276	18914.8	0.02554	29812.5	27793.2
	Slowed down data TOF calculated from cal parameters			TOF L#	VelocL26	E Beam	channel	MG_Ex	TKE
540		68Ni	2639	443.379	5.952	19.07	12352.1	1.5 MeV
540		68Ni	2150	384.1771	5.5963	16.93	12352.1	0 MeV	1159.9214 MeVu

---
LISE++ for slowed down beam
Measured v = 5.5963
LISE++ calculated = 5.6187
Brho 1.4380Tm

---
Another method is to check doppler correction Exogam
Beta for L21 calibration is 0,1825
Beta for L26 calibration is 0,1882

---
The problem, can be :
Wrong cable of tac : cats mixed with D6 (really low probablity)
Wrong listing of tac channel (I checked other tac channels T-DD6-DD4 and T-CATSD6-D4 from lise daq, it gives the same energy 19 MeV)
Lise tacs are not trustable, since there is an integration window problem most probably.

---
Mixing channel (most probable scenario since D6-D4 is 21 meter)
TAC_CATS_D4 → TAC_D6_D4 (lise)
TAC_D6_D4 (lise)→ TAC_CATS_D4
Then D6-D4 should give correct results in 26 meter

---
T-DD6-DD4
TOF = (Time_0_ref - TAC_DD6_DD4)*slope
			calculated				channels		Time 0 ref
Runexp	RunLISE	isotope	distance cm	TOF catsd4	distance cm	TOF L21	D4-D6	Slope	L26	L 21
507	432	68Ni	2639	318.542069521595	2150	259.51703276	32035	0.00749	74563	66659.9
503	425	68Ni	2639	278.518018184409	2150	226.9093365276	36663	0.00749	73823.8	66938
	Slowed down data TOF calculated from cal parameters			TOF L#	VelocL26	E Beam	channel	MG_Ex
540		68Ni	2639	414.16	6.3719	21.78	19268.7	2.5 MeV
540		68Ni	2150	354.96	6.057	19.6	19268.7	2 MeV

---
T-CATSD6-DD4
TOF = (Time_0_ref - TAC_CATSD6_DD4)*slope
			calculated				channels		Time 0 ref
Runexp	RunLISE	isotope	distance cm	TOF catsd4	distance cm	TOF L21	D4-D6	Slope	L26	L 21
507	432	68Ni	2639	318.542069521595	2150	259.51703276	24366.2	0.00691
503	425	68Ni	2639	278.518018184409	2150	226.9093365276	18279.3	0.00691
	Slowed down data TOF calculated from cal parameters			TOF L#	VelocL26	E Beam	channel	MG_Ex
540		68Ni	2639	414.16	6.3719	21.78	19268.7	2.5 MeV
540		68Ni	2150	354.96	6.057	19.6	19268.7	2 MeV

---
Integration gate
problem
During the analysis, I compare the Lise runs with zdd runs. Since we have the same signal, I was expecting to see same results for two tacs that we copy from them.
But I see such comparison during this analysis: there is shift in both channel and amplitude. Which simply can be explained by the signal attenuation. However if it is only attenuated, the shift (2770 ch) should be same for each run, while the situation is not like that.
Therefore, there is more serious issue here :

---
Possible scenario :
- Most probably, our integration gate is smaller than what he used, and we are integrating in the rise part of the logic signal, so there is lots of fluctuations, and the signal is not reliable.
- This scenario makes lise copy tacs, unreliable.

---
BACKUP
ASSUME 67Ni is not 67 Ni

---
T-CATS1-D4
			Notebook values			calculated				channels
Runexp	RunLISE	isotope	brho	Energy	velocity	distance cm	TOF catsd4	distance cm	TOFDD6-DD4	Cats-D4	DD6-DD4
507	432	68Ni	2.1671	37.7436	8.28462	2639	318.542069521595	2150	259.51703276	17240.0	32035.0
503	425	68Ni	2.5107	50.32794	9.47515	2639	278.518018184409	2150	226.9093365276	18914.8
Slope : -0.02388,
gain 730.0388
Tof; 435.054
velocity: 6.0659 Energy : 19.66
No change in beam energy

---
T-DD6-DD4
TOF = (T_DD6_DD4 -Time_ref_0)*slope
			calculated				channels		Time 0 ref
Runexp	RunLISE	isotope	distance cm	TOF catsd4	distance cm	TOF L21	D4-D6	Slope	L26	L 21
507	432	68Ni	2639	318.542069521595	2150	259.51703276	32035	0.00749	10464.9	2589.7
503	425	68Ni	2639	278.518018184409	2150	226.9093365276	36663	0.00749	73823.8	66938
	Slowed down data TOF calculated from cal parameters			TOF L#	VelocL26	E Beam	channel	MG_Ex
540		68Ni	2639	65.94	65	--------------	19268.7	2.5 MeV
540		68Ni	2150	124.92	17	--------	19268.7	2 MeV

---
T-CATS1-D4
TOF = (TAC_CATS1_D4 -Time_ref_0)*slope
			calculated				channels		Time 0 ref
Runexp	RunLISE	isotope	distance cm	TOF catsd4	distance cm	TOF L21	Cats-D4	Slope	L26	L 21
507	432	68Ni	2639	318.542069521595	2150	259.51703276	17240.0	0.02554	4767.71	6342
503	425	68Ni	2639	278.518018184409	2150	226.9093365276	18914.8	0.02554	29812.5	27793.2
	Slowed down data TOF calculated from cal parameters			TOF L#	VelocL26	E Beam	channel	MG_Ex
540		68Ni	2639	196.77452	13.44	110	12352.1	---
540		68Ni	2150	156.56	13.7326	116.666	12352.1	------

---
MG_Ex with TOF cuts

---
Green region

---
Blue region

---
Pink region